## Slide 1
Slide 1: Title Slide
Drift-Sense
AI-Powered Navigation-Error Recovery for Wafer Inspection Tools
Semicon India Hackathon 2026 — Applied Materials Problem Statement
Team: [TEAM NAME], Vellore Institute of Technology

## Slide 2
Slide 2: The Problem
## Pinpointing the Right Periodic Cell
Aspect | Detail
--- | ---
**Task** | Match a 100× native reference crop to a 10× search image
**Challenge** | Periodic layout → thousands of visually identical candidates
**Failure Mode** | NCC peak often lands on wrong periodic repeat
**Key Insight** | Problem is not *detection* — it is *disambiguation*
• Reference: 1000×1000 px at 100× magnification
• Search: 1000×1000 px at 10× magnification (~10× downsample)
• Nominal scale ratio: 10:1 (robustness tested 9:1 to 11:1)

## Slide 3
Slide 3: Why NCC Alone Fails
## The Periodic Ambiguity Problem
• NCC computes spatial cross-correlation → finds global maximum
• On periodic structures: correlation surface has **many near-equal peaks** at multiples of the pitch
• Global argmax often picks a decoy cell, not the true site
Three Canonical Failure Modes (Self-Eval Benchmark):
Sample | Error | Root Cause
--- | ---: | ---
`finfet_017` | 214 px | Stage-2 refinement converges to wrong periodic cell
`finfet_021` | 571 px | True site in top-K pool but misranked by NCC score
`finfet_023` | 868 px | True site absent from top-100 coarse peaks (98.5th percentile)
**All three correctly self-flagged as low-confidence** via ambiguity ratio.

## Slide 4
Slide 4: DriftSense V1 — Two-Stage NCC Baseline
## Production Algorithm
Stage 1: Coarse Global Search
• Single nominal-scale, zero-rotation NCC over full 1000×1000 search image
• Computes ambiguity ratio (best peak vs. best elsewhere) → confidence flag
Stage 2: Fine Local Refinement
• 5 scales × 7 rotations grid search in local window around Stage-1 peak
• Parabolic sub-pixel peak refinement
• **3× speedup** (21.9s → 7.2s) by confining grid to local window
Results (40 pairs: 15 DRAM + 15 FinFET + 10 OOD mixed_logic):
• ≤5 px: **92.5%** | Median error: **0.09 px**
• DRAM: 100% (15/15) | FinFET: 80% (12/15) | OOD: 100% (10/10)
• Runtime: ~132 ms/sample (CPU)

## Slide 5
Slide 5: DriftSense V2 — Top-K Candidate Pool
## Enabling Reranking Experiments
Global NCC → top-K NMS peaks → independent Stage-2 refinement → dedup on **refined** coordinates → ranked list
K | Candidate Recall @5px
--- | ---:
10 | 95%
20 | 95%
40 | 95%
• **Fixes** `finfet_021`: GT enters pool at 0.02 px error
• **Does not fix** `finfet_017` (Stage-2 corruption) or `finfet_023` (candidate generation failure)
• Final ranked accuracy = V1 (92.5%), but enables reranking experiments
• Runtime: ~3.37s/sample at K=40

## Slide 6
Slide 6: Experimental Journey — What We Tried & Rejected
Experiment | Hypothesis | Result | Why Rejected
--- | --- | --- | ---
**V3 Native Verification** | Native-res NCC re-ranks V2 pool | 67.5% @5px | Rescued `finfet_021` but **broke 11 DRAM cases** (100%→26.7%)
**Gradient (Sobel)** | Structural edges break periodicity | 37.5% / 70.0% | Helped `finfet_017` pool but failed globally
**Periodicity Signatures** (FFT/Gabor) | Layout frequency identifies cell | ~0% | Translation-invariant — tells structure, not occurrence
**V4 Phase Correlation** | Local phase separates true site | 87.5% @5px | Rescued `finfet_021` but **broke 3 correct DRAM cases** (noisy 30px window)
**Scientific Story**: *"We tested multiple increasingly domain-aware approaches and retained the robust baseline when they failed to generalize."*

## Slide 7
Slide 7: DriftSense V5 — Gated Phase Reranker (Production Default)
## Dual Gating Prevents Regressions
```python
if template_side >= 60px AND top2_score_margin < 0.01:
apply_phase_reranker() # Only on ambiguous FinFET candidates
else:
keep_v2_ranking() # DRAM / confident cases unchanged
```
**Rationale**: Phase correlation needs spatial support (~60px template). Works for FinFET (~100px) but fails on DRAM (~30px). Gate prevents DRAM regression.
Results (40 pairs):
• **95% @5px** overall (DRAM 100%, FinFET 93.3%, mixed_logic 100%)
• Runtime: ~200 ms/sample — minimal overhead over V1
• All 3 failure cases self-flagged; `finfet_021` rescued

## Slide 8
Slide 8: Dataset Design — Synthetic Benchmark with Realism
## Shared Canvas + Independent Degradation
• **Shared native canvas** (10k×10k): Reference = crop, Search = full downsample → GT true by construction
• **Breaking perfect periodicity**: Low-frequency brightness field + sparse defects + guaranteed landmark blobs (2-4 per crop, sized to survive 10× downsample)
• **Independent degradation**: Separate RNGs per image (noise, blur, rotation, scale)
• **SEM Physics** (all cited):
• Edge brightening (SE escape probability at topographic edges)
• Mixed Poisson-Gaussian noise (shot noise + read noise)
• Non-uniform brightness (charging/gain drift)

## Slide 9
Slide 9: Key Results Summary
## Robust, Fast, and Honest
Metric | V1 Baseline | V5 Gated (Default)
--- | ---: | ---:
**Overall @5px** | 92.5% | **95.0%**
DRAM @5px | 100% | 100%
FinFET @5px | 80.0% | **93.3%**
mixed_logic @5px | 100% | 100%
Median Error | 0.09 px | 0.08 px
Runtime (CPU) | ~132 ms | ~200 ms
Low-Confidence Flagging | 3/3 correct | 3/3 correct

## Slide 10
Slide 10: Known Limitations & Future Work
## Honest Assessment
1. **V5 is a strong but simple baseline** — learnable embeddings could beat it on hard periodic regions
2. **CPU-only throughput** — CUDA `cv2.cuda.matchTemplate` expected to give further speedup (not verified)
3. **Synthetic validation only** — noise/edge parameters cited but not validated against real SEM images
4. **finfet_023 unsolved** — GT absent from any NCC-based candidate pool; needs new signal (see SSJD proposal)

## Slide 11
Slide 11: SSJD — Next Algorithmic Contribution
## Semiconductor-Specific Joint Descriptor
**Core Idea**: FinFET has **two incommensurate frequencies** (fins ~4px, gates ~30px). Their **joint phase relationship** is physically fixed but varies across lattice cells.
• **Intensity NCC**: Uses Fourier *magnitude* → translation-invariant
• **Phase Correlation**: Uses Fourier *phase* but needs large template
• **SSJD**: Uses **joint phase coupling** between fin & gate lattices + topological moments of landmarks
**Breaks lattice translation invariance fundamentally** — not just locally like phase correlation.
**Expected**: Recovers `finfet_023` (unique global peak in SSJD surface) + generalizes to DRAM/mixed_logic via auto-detection.

## Slide 12
Slide 12: Thank You
## Drift-Sense: Robust Navigation-Error Recovery
Key Takeaways:
• Two-stage NCC + gated phase reranker → **95% @5px**, ~200ms, self-aware
• Systematic experimental journey: tried 4 advanced methods, kept the one that generalizes
• Synthetic benchmark with SEM physics realism + citations
• Clear path forward: SSJD for the remaining hard cases
**Repository**: github.com/[REPO] | **Contact**: [EMAIL]
Drift-Sense — Because the algorithm should know when it doesn't know.